LC3 Hardware Specification
# CPU
Z80A running at 3.5 Mhz.
IRQ is called at frame sync rate (50Hz), meant to be used in IM1.
# Memory
ROM “Cartridge” of up to 32k from $0000-$7FFF.
Do not assume partial decoding works.
The area from $1000-$13FF contains the ROM based user defined graphics (as well as the vectors), these are graphics numbers $00-$7F.
RAM Memory, 1k by default from $8000-$83FF.
This can be expanded as far as 64k.
# Graphics
The screen is a 32 x 20 character screen (640 bytes). The graphic numbers are stored at $8000-$827F.
The attributes are stored in 32 x 24 Nibbles (e.g. 384 bytes), these are stored from $8280-$83FF. The low byte is the left hand pixel. The 4 bit attributes are the same as the Spectrum (e.g. half bright).	.
RAM UDGs are stored from $8000-$83FF and are graphics numbers $80-$FF. However only $82C0-$82FF is actually available for this (the rest is character or colour RAM) which is chaacters 216-223 ($D8-$DF). In practice it is pretty desperate for RAM memory :)
Extra RAM can be extracted by setting all the attributes for a line to the same as the background ; that character code space is then available for use.
# Alternative behaviour with more RAM
The ‘extension’ flag does the following :-
1) Moves the attribute RAM to $8680-87FF ; mapping is otherwise unchanged. This allows the full 32x24 character display to be shown (it is truncated normall) which occupies $8000-$82FF.
2) UDG RAM space is moved from $8000-$83FF to $8400-$87FF
## Mapping a Graphics Cell Address to an Attribute Address
This requires a little bit of tweaking, but it is not difficult.

Action	Cell start	Cell end
Start value	$8010	$8210
Make it an offset from start	$0010	$0210
Shift Right once (bytes → nibbles) – carry describs nible half	$0008	$0108
Xor address High with $83	$8308	$8208
Xor address Low with $80	$8388	$8288

The range for attributes maps $000-$280 (screen) onto $280-$3FF. (attrobute)
# Other Devices
Standard Sinclair Joystick (port $FE)
Beeper (port $FE)
Cassette I/O as per the Sinclair specification (port $FE)