LC3 Hardware Specification
# CPU
Z80A running at 3.5 Mhz.
IRQ is called at frame sync rate (50Hz), meant to be used in IM1.
# Memory
ROM “Operating system” of 8k from $0000-$1FFF
ROM “Cartridge” of up to 24k from $4000-$7FFF.
RAM Memory, 1k by default from $8000-$83FF (not properly decoded). The 1k RAM can be disabled.
This can be expanded as far as 64k.
OSEN = A15+A14+A13 = 0 (can be disabled using extension#2 flag)
ROMEN = !OSEN – because of the partial decoding (a 4k ROM would be mapped into memory 8 times).
Character memory is read via 7C00-7FFF (the top 1k) e.g. !OSEN and using the internal decoding of the ROM chip.
# Graphics
The screen is a 32 x 20 character screen (640 bytes). The graphic numbers are stored at $8000-$827F. (It can be extended to 32x24)
The attributes are stored in 32 x 24 Nibbles (e.g. 384 bytes), these are stored from $8680-$87FF. The low byte is the left hand pixel. The 4 bit attributes are the same as the Spectrum (e.g. half bright).	.
RAM UDGs are stored from $8800-$8BFF in theory and are graphics numbers $80-$FF.
In practice all this is packed into the same 1k. Because not all attributes are displayed when all in 1k a small area of RAM ($8680-$86BF mapped onto $8280-$82BF) is free, UDGs $D0-$D7, this is unrequired attribute area.
This should be accessed via $8E80-$8EBF ; in 4k mode this will be free memory, in 1k mode it will map onto that free space.
For more RAM set a row of attributes to background (or half a row, or whatever) which will free the mapping character rows.
# Other Devices
Standard Sinclair Joystick (port $FE)
Beeper (port $FE) (bit 7 set means only display 20 lines)
Cassette I/O as per the Sinclair specification (port $FE)

## Memory Maps
This shows how using partial decoding allows consistent addressing of memory whether the base 1k machine or higher. The addresses on the right ($8000,$8680,$8800 and $8E80) are used with 4k+ expansion memory and are the physical addresses used by the hardware, but map onto the correct addresses with 1k memory with 32 x mirroring.

Note that (for example) $86C0 will actually write to $8280 on a 1k RAM machine.

Range	1k Memory	4k + Memory
0000 / 3FFF	Built in ROM (can be disabled by cartridge line)
4000 / 7FFF	Cartridge program memory (24k). Memory addressed by 7C00-7FFF is the lower 128 characters. This could be at the end of the ROM (4k) or in the middle (8k)
8000 / 827F	Character RAM (32x20).	Character RAM (32x24).
8280 / 82BF	Free / UDG RAM
82C0 / 83FF	Attribute RAM (32x20)	Free
8400 / 867F	Mirrored (1k)	Free
8680 / 87FF	Access attribute RAM 82C0-83FF via mirroring.	Attribute RAM (32x24)
8800 / 8BFF	Access 8 UDGs 8280-82BF via mirroring	128 UDG Memory (1k)
8C00 / 8E7F	Mirrored (1k)	Free
8E80 / 8EBF	Access for the 64 byte memory gap in 1k RAM 8280-82BF by mirroring (code/data)	Free, remembering this 64 byte slot is mapped here.f
8EC0 / 8FFF	Mirrored (1k)	Free
9000 / FFFF	Mirrored (1k)	Expansion if > 4k